## Slide 1
Data access
Need SLC products Source: ASF, CopHub etc
Data organisation
Delivered S1 SLC scenes do not consistently have the same coverage. Either do further processing at the “burst” level, or form new scenes from sets of bursts). The latter approach was used at GA
Co-registration of reference SLC to DEM
This mapping is used later for interferogram geocoding
Co-registration of other SLCs to reference
The co-registration of each S1 image needs to be better than 1/1000th of a pixel to avoid burst discontinuities. GA implemented a tree network structure to apply co-registrations and avoid propagating mis-registration in a large multi-year stack of 12 day images.
Interferogram formation
Typically done with an “SBAS” network where every SAR image is used to form multiple interferograms for redundancy of information
Interferogram unwrapping
Convert fringes to continuous phase field using unsupervised algorithm like snaphu of MCF. These are good for automation but they do make mistakes (unwrapping errors)
Geocoding
Convert products (interferograms, coherence, backscatter) from radar to geographic geometry
Unwrapping check
Throw out pixels that fail the check – removes unwrapping errors
Orbital error removal
Model long wavelength spatial trends and remove. Usually not that important for S1
Atmospheric noise removal
Various approaches, best use external weather model data to generate a phase correction
Network inversion for displacement time series
Pixel-wise process
Network inversion for average displacement
Pixel-wise process for velocity
High level components of an InSAR processing pipeline
InSAR software: SNAP, Gamma, GMTSAR, ISCE etc
Time series software: StaMPS, PyRate, MintPy, LicSAR etc

## Slide 2
Data access
Need SLC products Source: ASF, CopHub etc
Data organisation
Las escenas S1 SLC entregadas no tienen siempre la misma cobertura. O bien se realiza un tratamiento posterior a nivel de " burst " o bien se forman nuevas escenas a partir de conjuntos de bursts. Este último enfoque se utilizó en GA
Co-registration of reference SLC to DEM
Esta cartografía se utiliza posteriormente para la geocodificación de interferogramas
Co-registration of other SLCs to reference
El corregistro de cada imagen S1 debe ser mejor que 1/1000 de píxel para evitar discontinuidades de burst. GA implementó una estructura de red en árbol para aplicar corregistros y evitar la propagación de errores de registro en una gran pila multianual de imágenes de 12 días.
Interferogram formation
Normalmente se hace con una red "SBAS" en la que cada imagen SAR se utiliza para formar múltiples interferogramas para la redundancia de la información.
Interferogram unwrapping
Convertir las franjas en un campo de fase continua utilizando un algoritmo no supervisado como snaphu de MCF. Son buenos para la automatización, pero cometen errores (errores de desenvoltura).
Geocoding
Convert products (interferograms, coherence, backscatter) from radar to geographic geometry
Unwrapping check
Descarta los píxeles que no superan la comprobación: elimina los errores de desenvoltura.
Orbital error removal
Modelar tendencias espaciales de longitud de onda larga y eliminar. Normalmente no es tan importante para S1
Atmospheric noise removal
Varios enfoques, el mejor utiliza datos de modelos meteorológicos externos para generar una corrección de fase
Network inversion for displacement time series
Pixel-wise process
Network inversion for average displacement
Pixel-wise process for velocity
High level components of an InSAR processing pipeline
InSAR software: SNAP, Gamma, GMTSAR, ISCE etc
Time series software: StaMPS, PyRate, MintPy, LicSAR etc

## Slide 3: Preguntas
Bursts?
GA?
SLC?
Documentación inSAR
Investigar
  Co-registration
  “SBAS” network
  Unsupervised algorithm like snaphu of MCF
  Pixel-wise process
Entender el problema
Definir Objetivos
Crear Pipeline con imágenes
Crear Esquema de tareas
Preparar Glosario
Investigar de sobre los softwares
Tareas